## Slide 1
Welcome

## Slide 2: 21EC1202
COMPUTER ORGANIZATION AND ARCHITECTURE
CO3
Input / Output Devices

## Slide 3
Input / Output Devices: Introduction to input/output processing, working with video display unit and keyboard and routine to control them. Program controlled I/O transfer. Interrupt controlled I/O transfer, DMA controller. Secondary storage and type of storage devices. Introduction to buses and connecting I/O devices to CPU and memory, TRAP and Interrupts
Input / Output Devices

## Slide 4: Input / Output
The computer system's input/output (I/O) architecture is its interface to the outside world.
The two important modules of the computer system -
The processor and
The memory module.
The third key component of a computer system is a set of I/O modules
Each I/O module interfaces to the system bus and controls one or more peripheral devices.

## Slide 5: Input / Output
There are several reasons why an I/O device or peripheral device is not
directly connected to the system bus?
There are a wide variety of peripherals with various methods of operation.
The data transfer rate of peripherals is often much slower than that of the memory or processor.
Peripherals often use different data formats and word lengths than the computer to which they are attached

## Slide 6: Input/output Modules
The major functions of an I/O module are categorized as follows –
Control and timing
Processor Communication
Device Communication
Data Buffering
Error Detection

## Slide 7: Input/output Modules
Control & timings
The I/O function includes a control and timing requirement to co-ordinate the flow of traffic between internal resources and external devices.

## Slide 8: Input/output Modules
The control of the transfer of data from an external device to the processor might involve the following sequence of steps –
The processor interacts with the I/O module to check the status of the attached device.
The I/O module returns the device status.
If the device is operational and ready to transmit, the processor requests the transfer of data, by means of a command to the I/O module.
The I/O module obtains a unit of data from external device.
The data are transferred from the I/O module to the processor.

## Slide 9: Input/output Modules
Processor & Device Communication
During the I/O operation, the I/O module must communicate with the processor and with the external device
Processor communication involves the following:
Command decoding
Data
Status Reporting
Address Recognition

## Slide 10: Input/output Modules
Processor communication involves the following:
Command decoding :The I/O module accepts command from the processor, typically sent as signals on control bus.
Data :Data are exchanged between the processor and the I/O module over the data bus.

## Slide 11: Input/output Modules
Status Reporting :Because peripherals are so slow, it is important to know the status of the I/O module. For example, if an I/O module is asked to send data to the processor(read), it may not be ready to do so because it is still working on the previous I/O command. This fact can be reported with a status signal. Common status signals are BUSY and READY.
Address Recognition :Just as each word of memory has an address, so thus each of the I/O devices. Thus an I/O module must recognize one unique address for each peripheral it controls.

## Slide 12: Input/output Modules
Device communication: On the other hand, the I/O must be able to perform device communication. This communication involves command, status information and data.
Data Buffering
An essential task of an I/O module is data buffering
The data buffering is required due to the mismatch of the speed of CPU, memory and other peripheral devices.
So, the I/O modules store the data in a data buffer and regulate the transfer of data as per the speed of the devices.

## Slide 13: Input/output Modules
Error Detection
Another task of I/O module is error detection and for subsequently reporting error to the processor.
One class or error includes mechanical and electrical malfunctions reported by the device (e.g. paper jam).
Another class consists of unintentional changes to the bit pattern as it is transmitted from devices to the I/O module.

## Slide 14: Block diagram of I/O Module
Control & timings
The I/O function includes a control and timing requirement to co-ordinate the flow of traffic between internal resources and external devices.

## Slide 15: Input/output Modules

## Slide 16: I/O Operations
Two types of addressing are possible
Memory-mapped I/O
Isolated or I/O mapped I/O

## Slide 17: Memory-mapped I/O
There is a single address space for memory locations and I/O devices
The processor treats the status and address register of the I/O modules as memory location and the same machine instructions are used to access both memory and I/O devices.
For example, if the size of address bus of a processor is 16, then there are 216 combinations and all together 216 address locations can be addressed with these 16 address lines.

## Slide 18: Memory-mapped I/O
Since I/O devices are included in the same memory address space, so the status and address registers of I/O modules are treated as memory location by the processor.
Therefore, the same machine instructions are used to access both memory and I/O devices.

## Slide 19: Isolated or I/O -mapped I/O
In this scheme, the full range of addresses may be available for both.
The address refers to a memory location or an I/O device is specified with the help of a command line.
In general command line is used to identify a memory location or an I/O device.

## Slide 20: Isolated or I/O -mapped I/O
If = 1, it indicates that the address present in address bus is the address of an I/O device.
If = 0, it indicates that the address present in address bus is the address of a memory location.
Since full range of address is available for both memory and I/O devices, so, with 16 address lines, the system may now support both 216 memory locations and 216 I/O addresses.

## Slide 21: Differences between Memory Mapped I/O & I/O Mapped I/O
S.No. | Memory Mapped I/O | I/O Mapped I/O
1 | I/O device is treated like a memory device and hence given a memory address. | I/O device is treated as an I/O device and hence given an I/O address.
2 | Both have same address space | Memory and I/O have separate address space
3 | Due to addition of I/O addressable memory become less for memory | All address can be used by the memory
4 | Same instructions can control both I/O and Memory | Separate instruction control read and write operation in I/O and Memory
5 | Normal memory address are for both | In this I/O address are called ports.
6 | Lesser efficient | More efficient due to separate buses
7 | Smaller in size | Larger in size due to more buses
8 | Simpler logic is used as I/O is also treated as memory only. | It is complex due to separate separate logic is used to control both.

## Slide 22: Differences between Memory Mapped I/O & I/O Mapped I/O
S.No. | Memory Mapped I/O | I/O Mapped I/O
9 | I/O device has a 20 bit Memory address. | I/O device has an 8 or 16 bit I/O address.
10 | I/O device is given MEMR# and MEMW# control signals | I/O device is given IOR# and IOW# control signals
11 | Decoding is more complex due to more address lines | Decoding is easier due to lesser address lines
12 | More gates add more delays hence slower | Works faster due to less delays
13 | Allows many more I/O devices as I/O addresses are now 20 bits. | Allows many more I/O devices as I/O addresses are now 20 bits.
14 | Popular technique in Microcontrollers | Popular technique in Microprocessors.
15 | Any register can be used to transfer data with the I/O device | ONLY AL/ AH/ AX registers can be used to transfer data with the I/O device
16 | I/O devices can now be accessed using any memory instruction. | I/O devices can only be accessed by IN and OUT instructions.